## Slide 1
AI-Powered Perovskite Solar Cell
Defect Detection System
Harshkumar Lalakiya – 2507019013
Sahil Soni - 2507019023
Guidance of –
Dr. Archana Chaudhari
Machine Vision(TEE7276)

## Slide 2
The Problem — Why This Matters
🔬 Manual SEM inspection
Slow, subjective & error-prone at scale
⚡ Efficiency bottleneck
Micro-defects drop solar efficiency by 30–50%
🏭 Industry gap
No unified automated QA pipeline for perovskites
📊 Global Perovskite PV Market → $1.2 Billion by 2030

## Slide 3
Project Objectives
01
Dual-Mode Annotation Pipeline
Manual canvas drawing + AI-assisted auto-labeling (OpenCV / YOLO / SAM)
02
Multi-Model Benchmarking
Train & compare 6 YOLO variants on real SEM perovskite data
03
Best-in-class mAP50
Achieve highest mAP50 = 0.422 using YOLO11m architecture
04
ONNX Real-time Deployment
Export to ONNX format; serve via FastAPI with <200ms latency
05
Full Web Application
Glassmorphic web UI with annotation, training & benchmark tabs

## Slide 4
Literature Review — CV Applications & Clustering
Ultralytics YOLOv8 (Jocher et al., 2023)
One-stage real-time detector. 52.9 mAP on COCO benchmark. Dominates speed-accuracy tradeoff.
→ Baseline for our YOLO family comparison
Segment Anything (SAM) (Kirillov et al., 2023)
Zero-shot segmentation via prompt. ViT-H backbone (630M params). Generalizes to microscopy images.
→ Integrated as 3rd auto-label option in our pipeline
SEM Defect Clustering (Kim et al., 2024)
k-Means + DBSCAN on 224×224 SEM patch feature vectors. No labeling needed for grouping.
→ Motivated our 224×224 patch splitting strategy
🔍 Research Gap: No unified annotation + training + deployment pipeline specifically for perovskite SEM defects.

## Slide 5
Literature Review — Deep Learning Object Detection Architectures
YOLOv8s
1-Stage
✅ Fast (160 FPS)
⚠ Lower mAP
YOLO11m ✅
1-Stage
✅ Fastest on SEM
⚠ Best mAP50=0.42
YOLO11m Architecture

## Slide 6
Dataset — Real SEM Perovskite Images
5
Defect Classes
224px
Patch Size
3,995
Max Instances (3D_Pinholes)
3-Way
Train / Val / Test Split
Chart: Class Instance Distribution
| PbI₂ | 3D_Pinholes | 3D-2D_Pinholes
Instances | 2910 | 3995 | 3661

## Slide 7
End-to-End System Architecture
📷 SEM Images
→
✏️ Annotation Engine
→
🔲 224×224 Patching
→
🤖 YOLO11m ONNX
→
🌐 FastAPI Backend
→
📊 Web Dashboard
↩ Auto-label Feedback Loop (OpenCV / YOLO / SAM)

## Slide 8
Methodology — Dual Annotation Pipeline
✏️ Manual Annotation
1. Load SEM image in canvas
2. Draw bounding box with mouse
3. Assign defect class label
4. Coordinate transform to YOLO format
5. Save normalized .txt label file
🤖 AI-Assisted Auto-Annotation
OpenCV
Grayscale → CLAHE → Threshold → Contours → YOLO boxes
YOLO
Model inference → Confidence filter → Write .txt labels
SAM
Prompt segmentation → Polygon → Bounding box extraction
Override toggle: Append OR Overwrite existing labels

## Slide 9
Methodology — Model Training & ONNX Export Pipeline
⚙️ Training Config
Epochs:
50
Image Size:
224 × 224 px
Batch:
Auto (GPU)
GPU:
NVIDIA RTX 3050
Framework:
Ultralytics YOLO
Export:
ONNX (best.onnx)
Serving:
FastAPI + uvicorn
Latency:
< 200 ms (ONNX)
YOLO11m Backbone — C3k2 + C2PSA blocks (MDPI Sensors 2025)

## Slide 10
Results — Multi-Model Performance Comparison
#1
YOLO11m
mAP50-95: 0.1905
#2
YOLO11s
mAP50-95: 0.1734
#3
YOLOv8s
mAP50-95: 0.1629
#4
YOLO11l
mAP50-95: 0.1602
#5
YOLOv8m
mAP50-95: 0.1535
#6
YOLOv8l
mAP50-95: 0.0891
🏆 YOLO11m = Best on all metrics

## Slide 11
Results — Precision-Recall & Training Curves (YOLO11m)
Precision-Recall Bubble Chart (bubble size = mAP50-95)
Training & Validation Loss / Metric Curves (50 epochs)

## Slide 12
Results — Confusion Matrix Analysis (YOLO11m)
✅ Strong Detections
3D_Pinholes: 229 correct 3D-2D_Pinholes: 260 correct
⚠️ Key Weakness
Background FPs: 598 total PbI₂ ↔ Background confusion
💡 Fix: Add augmentation & per-class diagnosis

## Slide 13
Live Web Application — FastAPI + ONNX Powered
Detect Defects Tab
Model Benchmark Tab
⚡ < 200ms ONNX Inference
🌙 Light / Dark Mode Toggle
✏️ Canvas Annotation + AI Overlay
📊 Live Model Benchmark Viewer

## Slide 14
Critical Evaluation — Strengths vs. Limitations
✅ STRENGTHS
› Modular pipeline: annotation → training → deployment
› ONNX export: fast inference without PyTorch at runtime
› Dual annotation: Manual + 3 AI-assisted methods
› Real SEM data (not synthetic) — domain-authentic
› Full web UI with benchmark & comparison tabs
⚠️ LIMITATIONS
› mAP50-95 = 0.19 — moderate (needs more data)
› 224×224 patches lose spatial context
› High background false-positive rate
› No augmentation pipeline implemented yet
› App path mismatch for metrics display

## Slide 15
Conclusion & Future Roadmap
📌 Key Conclusions
🏆 YOLO11m outperforms all 5 YOLO variants
🔧 Full annotation → training → deploy pipeline built
📡 ONNX server runs reliably on RTX 3050
🖊️ Dual-mode annotation accelerates labeling by ~3x
🌐 Web UI validated for lab-scale real-world use
🚀 Future Work Roadmap
Phase 1:
Image augmentation (flips, blur, contrast jitter)
Phase 2:
SAM polygon segmentation labels for all classes
Phase 3:
Cloud deployment with GPU auto-scaling
Phase 4:
Real-time SEM microscope video stream integration